## Slide 1: Future Diesel-like renewable fuels – A literature review
CEN/TC 19/WG 24 meeting – 26th April 2023
Roland Dauphin – Science Executive Fuels Quality & emissions
Mickaël Matrat - IFPEN

## Slide 2
  Context & objective
  Identification/Selection of relevant pathways
    LCA and TEA
    Production potential
  Evaluation of blending behaviour
  Blending opportunities
  Summary and conclusion
Contents
Reference box for additional comments

## Slide 3
  Commercial HDV transportation is primarily powered by internal combustion engines (ICE)
  Although electrification is proposed, long-distance transport will still significantly rely on ICE in the next 10 years
    To decarbonize these vehicles, the development and use of low-carbon fuels by 2030 is essential
  Goal: identify the relevant renewable diesel-like options for 2030 by considering the following aspects
   Sustainability and scalability by 2030
    Consider feedstock type and availability, production cost, process maturity and life-cycle greenhouse gas emissions as key parameters
   Compatibility with legacy and future fleet
    Consider combustion, after-treatment efficiency, hardware compatibility and durability as key parameters
    Limited to no modifications to the vehicles’ settings and hardware
   Fuel specifications adaptation?
    Need to adapt fuel specifications to allow higher blending ratio of renewable fuels in the conventional diesel ‘EN590’ pool and go beyond the blending wall?
Motivation

## Slide 4
Structure of the study
LCA & Eco assessment of selected novel components
Task 5. Stakeholders Interviews
Task 2. Combustion system compatibility
LCA & Eco assessment of selected energy paths toward FAME and paraffins
Blending optimisation with conv. fuels
Blending optimisation with conv. fuels
Task 6. Research needs & Conclusions
Task 1.
Task 3.
Task 4.
Focus of this presentation

## Slide 5
Selected pathways – Feedstock, process and product
Resource | Process | Product | Comments / Research needs
Lignocellulose | Fermentation ATD | Paraffinic distillate | Industrialised technology Flexibility to other products  diesel or kerosene optimisation impacts?
Lignocellulose | Gasification - FT | Paraffinic distillate | Technology close to industrialization - Optimisation prospects Flexibility to other products but integrability and adaptation to lignocellulose required
WCO / Animal fat / Energy crop oil | Hydrotreatment of triglycerides | Paraffinic distillate (HVO / HEFA) | Industrialised technology Application to a wider range of resources Integration of renewable H2?
WCO / Animal fat / Energy crop oil | Transesterification | FAME | Industrialised technology – adapted to small scale /close to resource Blending constrains
Lignocellulose | eFuel – Lignoc. | Paraffinic distillate | eH2 and RWGS technology to industrialise Optimisation prospects (electrolysers, CO2 capture, CO/CO2 from biomass) High flexibility to other fuels
CO2 | eFuel – CO2 | Paraffinic distillate | 
E-fuel
Focus on hybrid process

## Slide 6
LCA – TEA of selected pathways
The sensitivity to the resource can be very different for the energy pathways (ATD)
Best CO2 score for ATD and E-fuel
Good compromise for distillate from gasification + FT pathway
Best case

## Slide 7
Biomass conversion yields to renewable fuels
Pathway | Feedstock | Mass yield
Fermentation – AtD | Sugarcane | 9 ↔ 12%
Oil hydrotreatment | Waste cooking oils | 90 %
 | Lard and beef tallow animal fats | 92 ↔ 97%
Transesterifcation | Waste cooking oils | 83 ↔ 97%
 | Animal fats | 93 %
Gasification + Fisher-Tropsch | Biomass | 14 ↔ 26%
E-fuel from lignocellulose | Biomass + electricity | 47 ↔ 52%
Lignocellulose hydrotreatment | - | No data found
E-fuel from CO2 | - | No data found
Hypothesis : Full conversion of FT-wax into distillate

## Slide 8
Potential middle distillate production
Based on biomass availability by 2030
Pathway | Fuel | Feedstock | Projected feedstock (Mt) | Estimated advanced renew. fuel quantity (Mt) | Estimated advanced renew. fuel quantity (Mt)
 |  |  | Imp. Coll. data | Imp. Coll. data | Literature review
Fermentation – AtD | Paraffinic fuel | Solid industrial waste (secondary agro & forest industries) | 133  191 | - | 14.6  21.0
 |  | Agricultural residues (straw-like) | 137  165 | - | 15.1  18.2
 |  | Lignocellulosic crops (grassy) | 36  108 | - | 4.0  11.9
Oil hydrotreatment | HVO | Used Cooking Oil (UCO) | 3.1 | 2.6 | 2.8
 |  | Animal fats | 2.2 | 1.87 | 2.1
Transesterification | FAME | Used Cooking Oil (UCO) | 3.1 | - | 2.8
 |  | Animal fats | 2.2 | - | 2.0
Gasification + Fisher-Tropsch | Paraffinic fuel | Solid industrial waste (secondary agro & forest industries) | 133  191 | 27.9  40.1 | 26.6  38.2
 |  | Agricultural (woody) & forestry residues | 5  7 | 1.0  1.5 | 1.0  1.4
 |  | Lignocellulosic crops (woody) | 36  108 | 7.6  22.7 | 7.2  21.6
E-fuel from lignocellulose | Paraffinic fuel | Solid industrial waste (secondary agro & forest industries) | 133 191 | 53.2  76.4** | 66.5  95.5
 |  | Agricultural (woody) & forestry residues | 5  7 | 2  2.8** | 2.5  3.5
 |  | Lignocellulosic crops (woody) | 36  108 | 14.4  43.2** | 18  54
*Sustainable biomass availability in the EU, to 2050 – Imperial College London
**ICL report estimated advanced renew. fuel quantity as for 2050
Projected renewable fuel production assuming all the sustainable biomass* for bioenergy by 2030
Assuming availabitily of renew. electricity
Conservative approach with most mature techonolgies
New
New

## Slide 9
Renewable middle distillates production potential by 2030
Considering high TRL processes only, the renewable diesel production potential considering sustainable biomass availability by 2030 ranges between 57 and 88 Mtoe/y (i.e. 24-37% of demand for middle distillates which is estimated at 241 Mtoe out of 350 Mtoe for the transport sector in 2030)

## Slide 10
Renewable middle distillates production potential by 2030
Adding (former) regulatory objectives for RFNBOs (2.6% ener.), the renewable diesel production potential considering sustainable biomass availability by 2030 ranges between 92 and 123 Mtoe/y (i.e. 38-51% of demand for middle distillates in 2030)
Distillates production requirement in Mt (low resources mobilization and RFNBOs target)

## Slide 11
Evaluation of blending behaviour & opportunities
Characterisation of fuel variability
Definition of mixing rules (focus on cold flow properties but includes CN, FP, Density and Viscosity)
Blending optimisation with and without additives
Sensitivity from relaxed specifications
Gasification - FT | 
eFuel – lignoc. | 
eFuel – CO2 | 
Hydrotreatment Lignoc. | 
Hydrotreatment oil | 
Fermentation ATD | 
Transesterification | 
  Paraffins
  FT type of product
  Paraffins
  HDT type of product
  FAME
FT best and worst
HDT best and worst
Energy crops (EC)
Animal Fats (AF)
Waste cooking oil (WCO)
TRAN best and worst
Energy crops (EC)
Animal Fats (AF)
Waste cooking oil (WCO)

## Slide 12
Blending limits - Conservative approach (MODEC model)
Base fuel CFPP: -25°C / Spec. Limit: -20°C (Class F)
Chart: Hydrotreatment Product
| HDT EC (Worst) | HDT EC (Best) | HDT WCO (Worst) | HDT WCO (Best) | White Diesel (WCO)
EN590 | 0.0069 | 0.2453 | 0 | 0.2005 | 0.0075
EN590-extented | 0.0069 | 1 | 0 | 0.2005 | 0.0075
CFPP
20
-11
19
-44
21
Density and cold flow are the main constraints.
Not shown here but a different model would lead to 5-10 points increase once the CFPP is the limiting factor
Main advantage of extended specification is to be less density dependent for significant energy path (AF trans / HDT of energy crops / FT)
CFPP is the constraint otherwise and limits greatly the incorporation rate
FP can be a constraint for selected low-quality feedstocks (Worst HDT WCO/Trans AF)
Chart: Fischer-Tropsch Product
| FT (Worst) | FT (Best)
EN590 | 0.0532 | 0.3023
EN590-extented | 0.0532 | 1
CFPP
-22
0
Chart: Transesterification Products
| TRANS EC (Worst) | TRANS EC (Best) | TRANS WCO (Worst) | TRANS WCO (Best) | TRANS AF (Worst) | TRANS AF (Best)
EN590 | 0.0173 | 0.1535 | 0.043 | 0.043 | 0 | 0.24
EN590-extented | 0.0173 | 0.1535 | 0.043 | 0.043 | 0 | 1
CFPP
-20
14
2
2
-9
11

## Slide 13
Blending limits – Additive impact - Focus on EN590 boundaries
Base fuel CFPP: -25°C / Spec. Limit: -20°C (Class F)
Additivation only improves cold flow properties (Cetane number is not a limit)
The use of cold flow improver increases the blending ratio from about 5 to 20 points. The increase being lower for higher CFPP temperatures. Nevertheless, the density can become a constraint before this maximum increase is reached (e.g. TRANS WCO or EC, FT, HDT WCO).
CFPP
-22
0
Chart: Transesterification Products
| TRANS EC (Worst) | TRANS EC (Best) | TRANS WCO (Worst) | TRANS WCO (Best) | TRANS AF (Worst) | TRANS AF (Best)
Without additives | 0.0173 | 0.1535 | 0.043 | 0.043 | 0 | 0.24
With additives (Common Case) | 0.0475 | 0.2182 | 0.1178 | 0.1178 | 0 | 0.24
With additvies (Base Case) | 0.0989 | 0.2182 | 0.2453 | 0.1875 | 0 | 0.24
CFPP
-20
14
2
2
-9
11
Chart: Fischer-Tropsch Product
| FT (Worst) | FT (Best)
Without additives | 0.0532 | 0.3023
With additives (Common Case) | 0.146 | 0.3023
With additvies (Base Case) | 0.2063 | 0.3023
Chart: Hydrotreatment Product
| HDT EC (Worst) | HDT EC (Best) | HDT WCO (Worst) | HDT WCO (Best) | White Diesel (WCO)
Without additives | 0.0069 | 0.2453 | 0 | 0.2005 | 0.0075
With additives (Common Case) | 0.0188 | 0.2453 | 0 | 0.2453 | 0.0206
With additvies (Base Case) | 0.0392 | 0.2453 | 0 | 0.2453 | 0.0429
CFPP
20
-11
19
-44
21
For every “best” energy path, the density is either the first constraint or it becomes quickly the limit if the cold flow improver additive is used.
With additives (Best case: boost -10°C)
With additive (Common case: boost -5°C)
Without additive

## Slide 14
Insights into possible fuel specifications evolutions for an increased renewable content
Rapid CFPP increase at low blending ratio limiting the biocomponent concentration.
Adjusting the standards for CFPP may be difficult due to operating/logistic constraints.
Improving the cold flow properties of renewable diesel products through various means is potentially an important lever for maximizing the use of sustainable products.
Only one product identified is fully compatible with EN590 density range
Extending the EN590 density limits by ±10 kg/m3 (arbitrarily chosen for demonstration only) could lead to increase in the maximum blending ratio by about 15-25% (best case by 35%).
  CFPP and Density are the main constraining properties
  Figures below illustrate CFPP and density blending behavior for all energy paths identified

## Slide 15
Summary
FAME and Paraffins variabilities mainly affect cold flow properties and density
Resources
Processes
Renewable diesel fuels
Conv. resources
Advanced resources
Used oil or animal fats
  Lignocellulose
      agricultural & forestry residues
      woody and grassy energy crops (no oil)
      industrial residues (biomass residues)
  Atmospheric CO2 + renewable energy (Direct Air Capture)
  industrial off-gases (Concentrated CO2 sources)
Gasification + FT
E-Fuel – CO2
E-Fuel – Lignoc.
Hydrotreatment oil
Transesterification
Fermentation (ATF)
Hydrotreatment Lignoc.
Biomass and green H2 potential availability  Production potential up to 24-51% of expected middle distillate demand by 2030
Blending behavior estimation with conventional fuels could be further improved due to limited data for FAME/paraffins blends
Competition with other sectors especially for paraffins in the next decade
Processes upgrade potential/requirements:
pre-treatment/process opti for various feedstocks
H2 integration for further GHG reduction
Better LCA/TEA evaluation (standard for LCA)
Production capacity increase to convert biomass potential
Density is the main EN590 constraint for increasing renewable content. Cold flow property improvement can contribute to increase up to 20 points the renewable content but is feedstock dependent
Gasif+FT
HDT
TRANS
ATD

## Slide 16
  Concawe report
    https://www.concawe.eu/wp-content/uploads/Rpt-22-18.pdf
Read more

## Slide 17
Roland Dauphin
Roland.dauphin@concawe.eu
fuels@concawe.eu

## Slide 18: WP1.1 & WP1.2 – Energy paths review
(1) agricultural & forestry residues
(2) woody and grassy energy crops (ex. Carinata plant to oil)
(3) industrial residues (biomass residues)
(4) atmospheric CO2 + renewable energy (Direct Air Capture)
(5) UCO & animal fat
(6) industrial off-gases (Concentrated CO2 sources)
Sustainable components limited to Paraffinic and FAME components
Categories
  Lignocellulose
      agricultural & forestry residues
      woody and grassy energy crops (no oil)
      industrial residues (biomass residues)
  Triglycerides
      UCO & animal fat
      energy crops (ex. Carinata plant to oil)
  CO2
      atmospheric CO2 + renewable energy (Direct Air Capture)
      industrial off-gases (Concentrated CO2 sources)
  Transesterification
  Triglycerides hydrotreatment
  Fermentation
  Gasification + Fischer-Tropsch
  e-fuel

## Slide 19: Processes from lignocellulose
Lignocellulose
Crushing
Torrefaction
Pyrolysis
Filtration
FT
Hydrogenation/ Isomerisation
Diesel
SAF
Naphta
WGS
Solvent wash
CO2 extract
Absorption
Fluidified bed
Entrained bed
Air separation unit / Steamer
Fermentation
Ethanol
Lignocellulose
Oligomerisation
Hydrogenation/Fractionation
Diesel
Ren. Naphta
SAF
Dehydration
Separation
Hydrolysis
Lignocellulose
Separation
Diesel FAME
Oleochem.
Fermentation
(Esterification/ Transesterification)
(Purification)
Fermentation - ATD
Direct fermentation
to Fatty acids
Gasification - FT
Renew. elect.
Water
Lignoc.
Desalination
Pre-treatment
Electrolyser
Gasification
Biogas cleaning
FT
Hydrogenation/ Isomerisation
Diesel
SAF
Naphta
RWGS
eFuel – Lignoc.
Lignocellulose
Acid hydrolysis
Diesel
Hydrotreatment
Preparation
SAF
Pre-treatment
Condensation
Other
H2
Hydrotreatment
Lignoc.
FAME
Paraffinic Distillate
Paraffinic Distillate
Paraffinic Distillate
Paraffinic Distillate
Legend

## Slide 20: Processes from triglycerides AND CO2
Washing
Purification
Base Homogeneous Transesterification
Separation
Diesel FAME
Glycerol
Acid Esterification
Cake
Filtration
FFA distillation
Deacidification
Degumming
Washing/ Absorption
Alkali neutralization
Separation
Drying
(Polystyrene removal)
Bacteria treat.
WCO / Energy crop / Animal fat
Evaporation (alcohol recycling)
WCO / Animal fat / Energy crop
Pretreatment
Diesel
Hydro-isomerization ad Hydrocracking
Hydrogenation and Decarboxylation
SAF
H2
FAME
Transesterification
Hydrotreatment of triglycerides
Renewable electricity
Water
CO2
Desalination
Electrolyser
FT
Hydrogenation/ Isomerisation
Diesel
SAF
Naphta
RWGS
eFuel – CO2
Paraffinic Distillate (HVO)
Paraffinic Distillate
Legend

## Slide 21: Co-Processing Possibilities
Pathways | CP Possibility | Max CP Ratio identified in lit. | CP Input Location | Input Product | Comment | Ref.
Gasification + FT | Yes | 7% a | VD+HC | FT wax | Gasification -> FT -> wax -> VD+HC. Other locations possible but less favorable. | [5]
eFuel – CO2 | Yes | 7% a | VD+HC | FT wax | E-fuel -> FT -> wax -> VD+HC | [426]
eFuel – Lignoc. | Yes | 7% a | VD+HC | FT wax | E-fuel -> FT -> wax -> VD+HC | 
Fermentation (ATD) | Yes | 10% | Hydrogenation/FCC | Oligomerization product | ATD and ATJ follow the same process, so we can refer to the available options for ATJ. | [5]
Hydrotreatment of triglycerides | Yes | 25% b | Direct | Raw oil from Energy crops, waste cooking oil, animal fat | Co-processing of RSO/AGO, HTL/VGO. Requires novel catalysts. Efficiency and product quality (e.g., cold flow properties) of the co-processing still need to be improved to be competitive. | [6-9, 10]
Hydrotreatment Lignoc. | Not identified |  |  |  |  | 
Transesterification | Not identified |  |  |  |  | 
a assumed similar to Gasification+FT
b lab-scale results
CP | Co-processing | VD | Vacuum distillation | FT | Fischer–Tropsch | HC | Hydrocracking
ATD | Alcohol-to-Diesel | FCC | Fluid catalytic cracking | AGO | Atmospheric gas oil | VGO | Vacuum gas oil
RSO | Rapeseed oil | HTL | Hydrothermal liquefaction product |  |  |  | 
Nomenclature:
Notes: Jong, Sierk de; Hoefnagels, Ric; Faaij, André; Slade, Raphael; Mawhood, Rebecca; Junginger, Martin (2015): The feasibility of short-term production strategies for renewable jet fuels - a comprehensive techno-economic comparison. In Biofuels, Bioprod. Bioref. 9 (6), pp. 778–800. DOI: 10.1002/bbb.1613.
Doliente, Stephen S.; Narayan, Aravind; Tapia, John Frederick D.; Samsatli, Nouri J.; Zhao, Yingru; Samsatli, Sheila (2020): Bio-aviation Fuel: A Comprehensive Review and Analysis of the Supply Chain Components. In Front. Energy Res. 8, p. 110. DOI: 10.3389/fenrg.2020.00110.
Alves, C. M., Valk, M., de Jong, S., Bonomi, A., van der Wielen, L. A. M., and Mussatto, S. I. (2017). Techno-economic assessment of biorefinery technologies for aviation biofuels supply chains in Brazil. Biofuels Bioprod. Biorefining 11, 67–91. doi: 10.1002/bbb.1711
Mawhood, Rebecca; Gazis, Evangelos; Jong, Sierk de; Hoefnagels, Ric; Slade, Raphael (2016): Production pathways for renewable jet fuel: a review of commercialization status and future prospects. In Biofuels, Bioprod. Bioref. 10 (4), pp. 462–484. DOI: 10.1002/bbb.1644.
Tanzil, Abid H., et al. "Production of Sustainable Aviation Fuels in Petroleum Refineries: Evaluation of New Bio-Refinery Concepts." Frontiers in Energy Research (2021): 665.
Fogassy, Gabriella, et al. "From biomass to bio-gasoline by FCC co-processing: effect of feed composition and catalyst structure on product quality." Energy & Environmental Science 4.12 (2011): 5068-5076.
Carmona, H. D. P., Akhmetzyanova, U., Tišler, Z., & Vondrova, P. (2020). Hydrotreating atmospheric gasoil and co-processing with rapeseed oil using supported Ni-Mo and Co-Mo carbide catalysts. Fuel, 268, 117363.
de Paz Carmona, H., Svobodova, E., Tišler, Z., Akhmetzyanova, U., & Strejcova, K. (2021). Hydrotreating of Atmospheric Gas Oil and Co-Processing with Rapeseed Oil Using Sulfur-Free PMoCx/Al2O3 Catalysts. ACS omega, 6(11), 7680-7692.
Badoga, S., Alvarez-Majmutov, A., Xing, T., Gieleciak, R., & Chen, J. (2020). Co-processing of hydrothermal liquefaction biocrude with vacuum gas oil through hydrotreating and hydrocracking to produce low-carbon fuels. Energy & Fuels, 34(6), 7160-7169.
https://www.sciencedirect.com/science/article/pii/S0016236119309275
426. http://www.flexchx.eu/pdf/webinar2021/Presentations_Webinar_19012021.pdf

## Slide 22: Summary
Resource | Process |  | Comments / Research needs
Lignocellulose | Fermentation ATD | Paraffinic distillate | Industrialised technology Flexibility to other products  diesel or kerosene optimisation impacts?
Lignocellulose | Fermentation to oil | FAME | Limited industrialised projects Blending constraints
Lignocellulose | Gasification - FT | Paraffinic distillate | Technology close to industrialization - Optimisation prospects Flexibility to other products but integrability and adaptation to lignocellulose required
Lignocellulose | Hydrotreatment Lignoc. | Paraffinic distillate | Limited industrialised projects
WCO / Animal fat / Energy crop oil | Hydrotreatment of triglycerides | Paraffinic distillate (HVO / HEFA) | Industrialised technology Application to a wider range of resources Integration of renewable H2?
WCO / Animal fat / Energy crop oil | Transesterification | FAME | Industrialised technology – adapted to small scale /close to resource Blending constrains
Lignocellulose | eFuel – Lignoc. | Paraffinic distillate | eH2 and RWGS technology to industrialise Optimisation prospects (electrolysers, CO2 capture, CO/CO2 from biomass) High flexibility to other fuels
CO2 | eFuel – CO2 | Paraffinic distillate | 
Excluded.
Lim. 7 paths

## Slide 23: WP1.3 – LCA & TEA assessment
  (1) Transesterification
  (2) oil hydrotreatment
  (3) fermentation
  (4) gasification + Fischer-Tropsch
  (5) e-fuel
(1) Lignocellulose
(2) Energy crops
(3) atmospheric CO2 + renewable energy (Direct Air Capture)
(4) UCO & animal fat
LCA methodology (functional unit, system boundaries and allocation)
Value of the environmental impacts & the different sources of impacts (e.g. process steps)
Cost breakdown and breakeven price

## Slide 24: WP1.3 – LCA & TEA assessment Key take aways by 2030 for the main energy paths
Resources flexibility
A few industrialised pathways
(ex. hydrotreatment, transesterification)
High GHG reduction potential
Fuel cost
Resources variability and related pre-treatment
GHG reduction and potential further increase with CO2 capture or green H2
Know-how for intermediate products (alcohols) and fuels
E-fuel: ready by 2030? (CO2 capture/green H2 required)
Biomass mobilisation & Renew. Energy production are essential
Other impacts than CO2 (e.g. biodiversity)
LCA lacking of standard and limited consequential analyses
Competition with other sectors (ethanol as a chemical platform!)
Gasif + FT: high capital invest.
Strenghts
Opportunities
Threats
Weaknesses
The main challenge is to work on incentives that are required to overcome threats and consolidate opportunities

## Slide 25: CO2 impact per fuel pathway
Chart: g CO2-eq / MJ
| Wood chips* | Wood chips** | Corn stover | Agricultural residues | Sugarcane (stalks and straw) 1G-2G | date palm waste | sugarcane (bagasse and straw) + eucalyptus | sugarcane (energy-cane) + eucalyptus | Corn stover, switchgrass, and willow (electrolyse: dedicated wind electricity) | CO2 (electrolyse: dedicated wind electricity) | kernel oil & fatty acid distillates | PFAD (Palm Fatty Acid Distillate) | Tallow | Tail oil | WCO | mutton tallow | tallow oil (JRC) | WCO (JRC) | Alcool-to-diesel | Gasification-FT | Efuel | Hydrotreatment | Transterification
 | 1.6 | 10 | 21 | 14.9 | 24.8 | 7.65 | 10 | 10 | 4 | 2 | 18 | 10 | 10 | 7 | 37.38 | 17.81 | 13.8 | 8.3
*syngas fermentation to ethanol followed by fuel production via alcohol condensation (Guerbet reaction), dehydration, oligomerization, and hydrogenation
**syngas fermentation to ethanol followed by fuel production via carbon coupling/deoxygenation (to isobutene), oligomerization, and hydrogenation
Notes: We focus here only on the LCA results with the details of the ressource
For hydrothreatment , gasification and efuel the results are quite consistent
diversity of results (atj and transterification) due to differences in resources but also in impact calculation methods

## Slide 26: WP1.4 & 1.5 Competition and synergies
*Sustainable biomass availability in the EU, to 2050 – Imperial College London
Objective:
  Estimate the potential diesel production from biomass availability
  Identify potential competition with other sectors considering the “Fit for 55” package
Hypotheses:
  Diesel or distillate mass yields from literature review (data from WP1.3)
  Real production capacity which refers to current infrastructures is not considered
  Resource availability data from Imperial College (IC) report* has been used as reference
    Resource: It does NOT include any food & feed crop biofuels (1G) / for each specific resource displayed in the literature, resource type defined by IC have been considered for this analysis
    Scenarios: Scenario 1 and 3 evaluated by IC were considered
    Scope: Europe by 2030
Scenario 1 : Low mobilisation (LOW)
Scenario 3 : Enhanced availability through R&I & improved mobilisation (HIGH)
Notes: Mtoe is an acronym that stands for million or mega tonnes of oil equivalent. The unit quantifies the amount of energy released when burning one million tonne of crude oil. The respective Mtoe value of different fuels varies.
Scenario :
LOW : This scenario assumes low mobilisation of biomass for both 2030 and 2050
MEDIUM : Improved mobilisation of biomass in selected countries
HIGH : Inhanced availability of biomass through R&I and improved mobilization
All markets : including energy and non-energy sectors
Bioenergy : including only energy sector

## Slide 27: POTENTIAL PRODUCTION based on high Mob. biomass mobilisation VS GHG emissions
Maximum projected renewable fuel production quantity by 2030 for high energy pathways production previously identified namely Fermentation, Gasification + FT. The related feedstocks are listed in Annex IX A of RED II/2018.
Oil hydrotreatment and transesterification have been considered as negligible compared to other paths.

## Slide 28
Addition of e-fuel from lignocellulose assuming that the fit for 55 target is reached for RFNBOs with liquid fuels only. This includes 2.6% of the total energy demand (0.7% for aviation sector)
This hypothesis is also quite optimistic for transport availability considering that renewable H2 contribution to other sectors is included in the objective
POTENTIAL PRODUCTION including regulatory objectives for RFNBO by 2030

## Slide 29
Mass yield and GHG emissions
The sensitivity to the resource can be very different for some energy pathways
  Fermentation - AtD
  Transesterification – WCO
Oil hydrotreatment – WCO* | Transesterfication – WCO*
Oil hydrotreatment – animal fats* | Transesterfication – animal fats*
Gasification + FT | E-fuel from lignocellulose
Fermentation – ATD | 
Lignocellulosic biomass | GWP impact*** (g CO2-eq/MJ)
Wood chips* | 1.6
Wood chips** | 10
Corn stover | 21
Agricultural residues | 14.9
*syngas fermentation to ethanol followed by fuel production via alcohol condensation (Guerbet reaction), dehydration, oligomerization, and hydrogenation
**syngas fermentation to ethanol followed by fuel production via carbon coupling/deoxygenation (to isobutene), oligomerization, and hydrogenation
***See presentation WP1.3
WCO | GWP Impact*** (g CO2-eq/MJ)
WCO (China) | 37.4
WCO (JRC) | 8.3

## Slide 30: ENERGY DEMAND AND Renew. DIESEL PRODUCTION Capacity based on biomass availability BY 2030
RFNBOs (9.2 Mtoe): e-fuel or e-fuel from lignocellulose ?
Advanced biofuels (Annex IX) (7.8 Mtoe): could be supplied through all identified pathways
Waste oils (Annex IX part B) (6 Mtoe): could be supplied through oil hydrotreatment (5.1 Mtoe) or transesterification (4.2 Mtoe) but the limit may not be reached by 2030
The bar graphs cannot be added as some of the energy paths use the same resources

## Slide 31: Product Properties
Products variability collected from literature review (synthesis from WP 1.1 to 1.3)
a Assumed that the small gaps in CN from the standard could be eliminated by additives
Name | Density [kg/m3] | Cetane Number | Kinematic Viscosity [mm2/s] | Flash Point [dgC] | Cold Filter Plugging Point [dgC]
Hydrotreatment Products |  |  |  |  | 
HDT EC (Worst) | 780 | 80 | 3.6 | 140 | 21
HDT EC (Best) | 780 | 80 | 3.6 | 140 | -44
HDT WCO (Worst) | 780 | 71 | 3 | 42 | 19
HDT WCO (Best) | 780 | 71 | 3 | 61 | -11
White Diesel (WCO) | 753 | 77 | 3.5 | 116 | 20
Fischer–Tropsch Products |  |  |  |  | 
FT (Worst) | 770 | 70 | 3 | 59 | 0
FT (Best) | 790 | 70 | 3 | 59 | -22
Transesterification Products |  |  |  |  | 
TRANS EC (Worst) | 876 | 51 | 5.6 | 130 | 11
TRANS EC (Best) | 888 | 62 | 2.7 | 193 | -9
TRANS WCO (Worst) | 860 | 51(49) a | 5.3 | 135 | 2
TRANS WCO (Best) | 897 | 57 | 4 | 196 | 2
TRANS AF (Worst) | 830 | 51(50) a | 6.9 | 50 | 14
TRANS AF (Best) | 883 | 60 | 3.5 | 175 | -20
Coloring on Numbers:
(EU)EN590
(EU)EN590-extended
Outside both standards

## Slide 32: Mixing RULES
  Density [0]
  linear blending rule : density is a property that is weighted by volume
  Flash-point [1]
  Non-linear blending rule : the more volatile fraction has a greater influence
Viscosity [2]
  Non-linear blending rule : the fluid base has a predominant weight which gives the mixture a much lower viscosity than that calculated by volume weighting
Cetane number [0]
  linear blending rule is considered as a first approximation (HC components)
  CFPP [3]
  Non-linear blending rule: existing models mainly based on compositional descriptors (FAME, SFAME, unsaturated, long-chain suturation factors (LCSF)) and solid-liquid equilibrium.
Semwal & Varshney 1995, seems to be the best
MODEC-modified: could be a conservative option
Vrablik et al. 2019: Not favored
Research need identified as limited data exist for FAME/Paraffins blends

## Slide 33: Standards
 | (EU)EN590 |  | (EU)EN590-extended | 
 | EN590 + CFPP (Class F, -20℃) |  | EN590 + EN14214 + EN15940 + CFPP (Class F, -20℃) | 
Property | Min | Max | Min | Max
Density [kg/m3] | 820 | 845 | 765 | 900
Cetane Number | 51 | --- | 51 | ---
Flash Point [℃] | 55 | --- | 55 | ---
Kinematic Viscosity [mm2/s] | 2 | 4.5 | 2 | 5
CFPP [℃] | --- | -20 | --- | -20
  2 boundaries considered for common countries in Europe
Properties of the B7 Used | 
Density | 833
CN | 51
KV | 3.3
FP | 55
CFPP | -25
  Average properties considered for the diesel base fuel